## Slide 1
FINAL PROJECT REVIEW
AI-Powered RF Digital Twin Using
ADALM-PLUTO
Automatic modulation classification on real over-the-air signals
23AID203 – Software-Defined Communication Systems
Faculty: Kavitha K
GROUP A-16
B. Suryacharantej – CB.AI.U4AID25009
B. Sai Srikar – CB.AI.U4AID25006
P. Sathwik – CB.AI.U4AID25041
M. Neeraj – CB.AI.U4AID25031
Notes: Introduce the team and the project title. Say: In the mid review we showed the AI working on a dataset. Today we show the same AI working on a real radio, the ADALM-Pluto, over the air.

## Slide 2
Introduction
2
Wireless systems send information using different modulation schemes (AM, FM, BPSK, QPSK, QAM)
A receiver must know the modulation type before it can demodulate the signal
Automatic Modulation Classification (AMC) identifies the type directly from the received I/Q samples
Our project: an AI-based RF Digital Twin – validated on the RadioML dataset, then deployed on a real ADALM-Pluto SDR
RF signal (over the air)
I/Q samples (2 × 128)
1D CNN
Modulation type
Problem: How can an unknown RF signal be identified automatically and reliably – not only in simulation, but on real radio hardware?
Notes: Explain modulation simply: different ways of putting data onto a radio wave. A receiver must know the type before decoding. AMC does that automatically. Our project does it with a CNN, first on a dataset and now on a real radio.

## Slide 3
Literature survey
3
Paper (Year) | Platform | Method used | Key findings and gaps
Automatic Modulation Classification with Deep Neural Networks (2023) | MDPI – Electronics | CNN architectures with dilated convolution, statistics pooling and squeeze-and-excitation | Findings: Achieved strong AMC performance on RadioML 2018.01A; best model reached 98.9% peak accuracy. Gap: Focuses mainly on model architecture and dataset evaluation rather than real-time hardware implementation.
Real-time Modulation Classification Architecture in Software Defined Radio (2024) | ScienceDirect – Physical Communication | Low-complexity 1D CNN + SDR-based receiver | Findings: Demonstrated real-time AMC using SDR; CNN achieved fast inference suitable for real-time operation. Gap: Uses a more complete/complex receiver architecture; scope remains for a simpler AI-to-hardware workflow.
Modulation Recognition Based on Multi-modal Fusion of ResNet and Traditional Signal Processing (2025) | IEEE Xplore – IEEE MTT-S IWS | ResNet-18 + traditional signal processing + ADALM-PLUTO | Findings: Tested modulation recognition using ADALM-PLUTO; ResNet-18 achieved >98% accuracy with faster inference than ResNet-50. Gap: Uses a more complex multimodal approach compared with a simpler CNN-based pipeline.
A Novel Deep Learning Automatic Modulation Classifier with Fusion of Multichannel Information Using GRU (2023) | Springer Nature – Journal on Wireless Communications and Networking | GRU-based fusion of I/Q and amplitude/phase information | Findings: Combined I/Q and A/P features to improve AMC, especially at low SNR; evaluated using RadioML data with 128-sample inputs. Gap: Multi-channel feature fusion increases model complexity for practical deployment.
Our approach: a simple 1D CNN on raw 2 × 128 I/Q – validated on RadioML, then deployed and fine-tuned on a real ADALM-Pluto.
Notes: Four papers from our survey. The first got 98.9 percent on RadioML 2018 but only on the dataset, not on hardware. The second showed real-time AMC on an SDR but with a more complex receiver. The third used ADALM-Pluto with ResNet-18 and signal-processing fusion, which is more complex than our CNN. The fourth fused I/Q with amplitude and phase using a GRU, which helps at low SNR but adds complexity. Our project fills the gap with a simple 1D CNN on raw I/Q, validated on the dataset and then deployed and fine-tuned on a real ADALM-Pluto.

## Slide 4
Objectives – all achieved
4
✓
Train a CNN on raw 2 × 128 I/Q samples with separate training, validation and test sets
Achieved
✓
Configure the ADALM-Pluto to transmit and receive all 5 modulations over the air
Achieved
✓
Capture real-time I/Q samples and feed them to the trained CNN
Achieved
✓
Classify live RF signals in a real-time digital-twin dashboard
Achieved
✓
Evaluate real-time performance and compare dataset vs. hardware accuracy
Achieved
✓
Close the simulation-to-reality gap by fine-tuning the CNN on real Pluto data
Achieved
Notes: Read the six objectives. All six are complete; the last one, fine-tuning on real data, was added after we measured the gap between simulation and hardware.

## Slide 5
Methodology: the RF digital twin
5
VIRTUAL TWIN – simulation (mid review)
PHYSICAL TWIN – ADALM-Pluto hardware (now)
RadioML 2016.10a dataset
MATLAB generates the modulated waveform
2 × 128 I/Q frames
Pluto TX → antenna → air → antenna → Pluto RX
1D CNN
Frame + normalise to 2 × 128 I/Q
Predicted modulation
Same 1D CNN
Compare with dataset label
Live prediction vs. transmitted label
Measure the gap → fine-tune the CNN on real Pluto data → re-test on a fresh capture
Notes: Two halves of the twin. Left: the virtual side we had at mid review. Right: the physical side we built now, using the same CNN. Comparing them shows the gap, which we then close by fine-tuning.

## Slide 6
Hardware setup
6
Laptop
MATLAB R2026b
+ CNN
USB (data + power)
ADALM-Pluto
AD9363 SDR
TX1
RX1
915 MHz over the air
One board transmits and receives at the same time (full duplex)
TX and RX share one clock, so frequency offset is negligible
Antennas give a real wireless channel: noise, reflections
Component | Details
ADALM-Pluto | AD9363, 325 MHz – 3.8 GHz, 1 TX + 1 RX
2 SMA antennas | On TX1 and RX1, about 2 cm apart
USB cable | Micro-B data port: I/Q samples + power
MATLAB R2026b | Communications, DSP, Signal Processing and Deep Learning toolboxes
Support package | Communications Toolbox Support Package for ADALM-PLUTO Radio
Notes: Point to the diagram. One Pluto both transmits and receives. The laptop sends the waveform over USB, the TX antenna radiates it, the RX antenna picks it up 2 cm away, and the samples come back over USB to MATLAB and the CNN.

## Slide 7
What the receiver sees
7
Notes: These are real constellations captured over the air by our Pluto. Each modulation has a clear shape: BPSK a line, QPSK four clusters, WBFM a ring. The CNN learns these differences directly from the raw I/Q numbers.

## Slide 8
CNN architecture
8
Input
2 × 128
Conv1D 5 × 32
+ ReLU
Conv1D 5 × 64
+ ReLU
Global avg
pooling
Fully
connected (5)
Softmax
→ class
Training on RadioML (dataset)
70 / 15 / 15 split: training / validation / test
Adam, learning rate 0.001, mini-batch 128
Early stopping on validation loss (max 30 epochs)
5 classes, SNR ≥ 10 dB
Test accuracy: 85.25%
Fine-tuning on Pluto data (now)
Starts from the trained weights
Same 70 / 15 / 15 split on real Pluto frames
Learning rate 0.0005, early stopping
10,500 real + 5,000 RadioML training frames
About 11 k parameters – real time on a laptop CPU
Notes: The same small CNN from the mid review: two 1D convolution layers that slide pattern detectors along the I/Q signal, then pooling and a 5-way classifier. Only about eleven thousand parameters, so it runs in real time on a laptop.

## Slide 9
Training, validation and testing
9
Training 70%
Validation 15%
Testing 15%
Stratified split: every modulation (and every power level) appears in all three sets in the same proportion
Set | Purpose | RadioML CNN | Pluto fine-tuning
Training | The network learns from these frames | 17,500 frames ¦ 84.9% | 10,500 + 5,000 RadioML ¦ 99.7%
Validation | Checked during training: best model kept, early stopping | 3,750 frames ¦ 83.3% | 2,250 frames ¦ 99.5%
Testing | Used only once, after training | 3,750 frames ¦ 85.3% | 2,250 frames ¦ 99.6%
Fresh recording | New capture, new random data, never seen | - | 9,600 frames ¦ 96.7%
Training, validation and test accuracy agree within 1-2 points: the model generalises and does not over-fit.
Pluto recording: 25,000 frames (5 power levels). Train / val / test use the 3 strongest levels = 15,000 frames (10,500 / 2,250 / 2,250); the 2 weakest levels (10,000 frames, near noise) are used only to test accuracy vs SNR.
Notes: Explain the three sets. Training: the network learns from it. Validation: checked during training to keep the best version and stop early, so it does not memorise. Testing: used only once at the end for the reported score. We did this for both stages, and then tested on a completely new recording. Training, validation and test accuracy are within one or two points of each other, which shows there is no over-fitting.

## Slide 10
Live RF digital twin dashboard
10
Live run: QPSK transmitted, QPSK predicted with 96% confidence
I/Q frame: exactly what the CNN sees
Spectrum: about 170 kHz wide, ~35 dB above noise
Constellation: 4 QPSK clusters
Confidence bars: CNN probability per class
Frame accuracy: 99.5% of frames correct
Keys 1-5 switch the transmitted modulation live
All 5 modulations classified correctly in the live test with antennas
Notes: This is our live demo. The Pluto transmits one modulation, the CNN classifies every frame in real time, and the screen shows the result. Press keys 1 to 5 to switch modulation. In the live test with antennas, all five were classified correctly.

## Slide 11
Results: dataset vs. real hardware
11
85.25%
Simulation: RadioML test set
74.1%
Real signals: original CNN
96.7%
Real signals: fine-tuned CNN
-11.2 pts
simulation-to-reality gap
+22.6 pts
gained by fine-tuning on real data
9,600 frames
fresh recording, never used in training
Note: the 96.7% comes from an independent fresh recording (9,600 frames, never used for training or validation). The dataset and hardware numbers are measured under different conditions (RadioML: many simulated channels; ours: one short-range lab link after fine-tuning on that link), so they are not a like-for-like comparison.
Notes: The three key numbers. 85.25 percent on the RadioML test set, in simulation. The same CNN on real signals drops to 74.1 percent - the simulation-to-reality gap. After fine-tuning on real data it reaches 96.7 percent on a completely new recording. Do not claim it beats simulation: the dataset covers many simulated channel conditions, while our test is one short-range lab link that the network was fine-tuned on, so the numbers are not directly comparable.

## Slide 12
Accuracy per modulation (real signals)
12
Chart: Independent fresh capture, 1,920 frames per class
| AM-DSB | BPSK | QAM16 | QPSK | WBFM
Original CNN | 4.4 | 99.4 | 98.1 | 94.7 | 74.1
Fine-tuned CNN | 91 | 98.9 | 98.6 | 99.8 | 95.3
Digital modulations (BPSK, QPSK, QAM16) were already above 94%
AM-DSB: 4% → 91% (+87 pts)
WBFM: 74% → 95% (+21 pts)
Analog signals change most between simulation and real hardware, so they gain most from real training data
Notes: Digital modulations were already strong for the original CNN. The big gains are the analog ones: AM-DSB from 4 to 91 percent and WBFM from 74 to 95 percent, because their real-hardware appearance differs most from the simulated data.

## Slide 13
Confusion matrix: before fine-tuning
13
How to read it
Row = what was really sent (1,920 frames each)
Column = what the AI guessed
Blue diagonal = correct
Red box = mistake
What it shows
Digital (BPSK, QAM16, QPSK): already 95-99% correct
AM-DSB: only 84 of 1,920 right (4.4%) – mostly called QAM16 (723) or WBFM (707)
WBFM: 479 called AM-DSB
Notes: Explain how to read it: each row is what was really sent, 1,920 frames per row; each column is what the AI guessed; the blue diagonal is correct and red boxes are mistakes. Before fine-tuning, the digital modulations are already fine, but AM-DSB is almost always wrong: only 84 of 1,920 correct, mostly called QAM16 or WBFM. WBFM is often called AM-DSB. Overall 74.1 percent.

## Slide 14
Confusion matrix: after fine-tuning
14
What changed
AM-DSB correct: 84 → 1,747 (91.0%)
WBFM correct: 1,422 → 1,830 (95.3%)
QPSK correct: 1,819 → 1,917 (99.8%)
Overall: 9,287 of 9,600 = 96.7%
Mistakes left
AM-DSB vs. WBFM (167 + 90): both analog, same audio
QAM16 vs. QPSK (26 + 3): QPSK points look like QAM16 corners
Fixed by deciding over more frames (next slide)
Notes: After fine-tuning on real Pluto data the diagonal is strong for every class: 9,287 of 9,600 frames correct, 96.7 percent. AM-DSB went from 84 to 1,747 correct. The remaining mistakes are mostly AM-DSB versus WBFM, because both are analog and carry the same audio, and a few QAM16 versus QPSK, because QPSK points look like the corners of QAM16.

## Slide 15
Deciding over more frames
15
96.7%
1 frame
0.13 ms of signal
99.5%
Vote of 8 frames
1 ms of signal
100%
Vote of 64 frames
8 ms of signal (live dashboard)
Same fresh recording (9,600 frames), fine-tuned CNN
AM-DSB: 91.0% per frame → 99.6% with 8 frames → 100% with 64 frames
WBFM: 95.3% per frame → 97.9% with 8 frames → 100% with 64 frames
8 ms is still instant for a person – this is how the live dashboard reaches 5 / 5 correct
Notes: One frame is only 0.128 milliseconds of signal. If the system takes a majority vote over consecutive frames, the remaining AM-DSB and WBFM mistakes disappear: 99.5 percent with 8 frames and 100 percent with 64 frames, which is only 8 milliseconds. The live dashboard already averages 64 frames.

## Slide 16
Thank you
Group A-16 | B. Suryacharantej – B. Sai Srikar – P. Sathwik – M. Neeraj
Notes: Thank the panel and invite questions. Be ready to run the live dashboard if asked.