## Slide 1
MID-PROJECT REVIEW :
AI-Powered RF Digital Twin Using
ADALM-PLUTO
23AID203 - Software-Defined Communication Systems
Faculty: Kavitha K
B SAI SRIKAR – CB.AI.U4AID25006
B SURYA – CB.AI.U4AID25009
P SAI SATHWIK – CB.AI.U4AID25041
M NEERAJ – CB.AI.U4AID25031
GROUP: 16

## Slide 2
Introduction
Modern wireless systems use different modulation techniques to transmit information.
When an unknown RF signal is received, its modulation type needs to be identified.
Automatic Modulation Classification (AMC) performs this identification automatically.
RF signals can be represented using In-phase (I) and Quadrature (Q) samples.
Deep learning can learn modulation-specific patterns directly from I/Q data.
This project develops an AI-based RF Digital Twin for modulation classification.
CONCEPT FLOW
RF Signal
I/Q Samples
CNN Model
Modulation Type
2

## Slide 3
Problem Statement
Manual signal identification is difficult for large numbers of RF signals.
Conventional approaches often depend on handcrafted signal features.
An AI-based classifier can learn patterns from I/Q samples and predict the modulation type
TARGET MODULATION
AM-DSB
BPSK
QAM16
QPSK
WBFM
3
How can an unknown RF signal be automatically identified from its I/Q samples using an AI model?

## Slide 4
Objectives
1
Collect RF signal samples from the dataset.
2
Extract and preprocess I/Q samples from the dataset.
3
Train a CNN model for automatic modulation classification.
4
Classify five modulation types using the trained model.
5
Implement and validate the classification system in MATLAB/Simulink.
4

## Slide 5
Literature Survey
5
Paper (Year) | Platform | Method Used | Key Findings & Gaps
Automatic Modulation Classification with Deep Neural Networks (2023) | MDPI | Deep CNN | Findings: • High AMC performance on RadioML 2018.01A • Best model reached 98.9% peak accuracy Gap: Focuses mainly on modulation classification , No real-time hardware implementation.
Real-time Modulation Classification Architecture in Software Defined Radio (2024) | ScienceDirect | 1D CNN+SDR | Findings: • Demonstrated real-time AMC using SDR • CNN can classify signals in real time. Gap: Receiver setup is complex.
Modulation Recognition using ResNet + Signal Processing (2025) | IEEE Xplore | ResNet + ADALM-Pluto | Findings: Tested modulation recognition using ADALM-PLUTO• ResNet-18 achieved >98% accuracy Gap: Model is more complex than our CNN.
Deep Learning AMC using GRU (2023) | Springer Nature | GRU + I/Q features | Findings: Combined I/Q and A/P features to improve AMC, especially at low SNR • Evaluated using RadioML data with 128-sample inputs Gap: Uses multiple features, increasing complexity.

## Slide 6
Research Gap
LIMITATIONS IN EXISTING APPROACHES
“Develop a digital-twin workflow that first validates AI-based modulation classification using RadioML I/Q samples, and subsequently transfers the same classification pipeline to real-time ADALM-Pluto I/Q data.”
6
Paper | Gap | Our Solution
2023 | Mainly dataset/model evaluation | Validate the CNN in MATLAB/Simulink and prepare it for ADALM_PLUTO
2024 | Relatively complex real-time receiver architecture | Use a simpler CNN-based classification pipeline
2025 | Complex ResNet + signal-processing fusion | Use a simpler CNN pipeline with direct I/Q input
2023 | Multi-feature fusion increases complexity | Use raw 2 × 128 I/Q samples as the CNN input

## Slide 7
Methodology
CURRENT(Simulation using Data Set )
RadioML Dataset
Sample Selection
I/Q Data (2 × 128)
CNN Model
Modulation Prediction
Comparison with Dataset Label
(FUTURE WORK (ADALM-PLUTO implementation)
ADALM-PLUTO
Real-Time RF Signal
7

## Slide 8
Work Completed
Dataset collected and loaded (RadioML 2016.10a dataset from DeepSig )
I/Q samples extracted and preprocessed
Five modulation classes selected
CNN model trained and evaluated
85.86% classification accuracy achieved
MATLAB/Simulink model developed
Sample number-based signal selection implemented
I/Q values, SNR, actual label and AI prediction verified in simulink
2

## Slide 9
Current Results
85.86%
Current Model Accuracy
5
Modulation Classes
2 × 128
I/Q Input Format
MATLAB /
Simulink
Demonstration Platform
Dataset :Click Here
9
Sample No → CNN → AI Prediction
↓
Actual Label
↓
I / Q / SNR
SAMPLE | Actual | AI PREDICTION | SNR
1 | QPSK | QPSK | 2 dB
2001 | AM-DSB | AM-DSB | -4 dB
16001 | BPSK | BPSK | 4 dB
9001 | QAM16 | QAM16 | 2 dB
12001 | WBFM | WBFM | -18 dB

## Slide 10
Future Work
1
Connect and configure the ADALM-Pluto for RF signal reception.
2
Capture real-time I/Q samples using ADALM-Pluto.
3
Feed the captured I/Q samples
4
Finding live RF signals using the trained AI model
5
Evaluate the real-time classification performance.
6
Hardware / software integration and final validation
7
Performance comparison: dataset-based vs. real-time classification
10

## Slide 11
Conclusion
An AI-based automatic modulation classification system was developed using the RadioML dataset.
I/Q samples were processed and classified using a CNN model.
The model achieved 85.86% classification accuracy across five modulation classes.
The complete dataset-based classification workflow was implemented and validated in MATLAB/Simulink.
The system is now ready for the next stage: real-time RF signal acquisition using ADALM-Pluto.
85.86%
Model Accuracy
5
Modulation Classes
RadioML
Current Data Source
ADALM-Pluto
Final-Stage Hardware

## Slide 12
References
Harper et al., Automatic Modulation Classification with Deep Neural Networks, Electronics, 2023.
Le et al., Real-time Modulation Classification Architecture in Software Defined Radio, Physical Communication, 2024.
Lai et al., Modulation Recognition Based on Multi-modal Fusion of ResNet and Traditional Signal Processing, IEEE MTT-S IWS, 2025.
Sun & Wang, A Novel Deep Learning Automatic Modulation Classifier with Fusion of Multichannel Information Using GRU, Wireless Networks, 2023.
RadioML Dataset — dataset used for the current implementation.
Analog Devices — ADALM-Pluto documentation.
12

## Slide 13
THANK YOU
Subject: Software-Defined Communication Systems